School Bus Vehicle Pre-Trip Walk-Around Inspection

and Inside Safety Checks

| INSIDE SAFETY CHECKS |
| --- |
| ( Steering Wheel | ( Windshield Wipers | ( Crossing Arm Control |
| ( Directional Signals | ( All Warning Lights | ( Driver’s Seat and Seat Belt |
| ( Horn Button | ( Brake Pedal and Brake | ( Mirrors |
| ( Oil Pressure Gauge | Warning Light | ( Windshield |
| ( Ammeter | ( Clutch Pedal | ( Side Glass |
| (Generator/Alternator) | ( Gear Shift Lever | ( Fire Extinguisher |
| ( Water Temperature Gauge | ( Neutral Safety Switch | ( First Aid Kit |
| ( Fuel Gauge | ( Parking Brake | ( Fuses and Emergency |
| ( Vacuum or Air Pressure Gauge | ( Daytime Running Lights | Equipment |
| ( Defroster | ( Headlights | ( Emergency Door and Buzzer |
| ( Windshield Washer | ( Hazard Warning | ( Clean Bus |
| ( Service Door Control | ( Stop Arm Control | ( Interior Lights |
| School buses should be checked before placing bus in service, or following the day’s run. All faulty or improperly functioning equipment should be promptly reported, in writing, to proper authorities so that maintenance personnel can be notified and the condition repaired. |

SCHOOL BUS PRE-TRIP INSPECTION CHECKLIST

| 1. Look Outside the Bus ___ Inspection decal up-to-date? ___ Windshield, mirrors, front windows, headlights – wipe clean ___ Front and rear bumpers secure ___ Rear emergency door, open and close ___ Bump tires. Ok? Lug nuts in place? ___ Suspension – cracked or broken parts? ___ Drain air brake tank ___ Look under bus – all clear? ___ General outside appearance, clean for school bus identification? ___ Washer fluid level ___ With engine COLD, check radiator coolant level ___ Engine oil level ___ Fuel tank, fuel lines for leaks and security 2. Electric Assist Brake Motor ___ Check electric motor operation ___ Check buzzer and warning light 3. Starting the Engine ___ Check ABS warning device ___ Check brake pressure differential warning light ___ Fuel gauge ok? Check brake warning buzzer, neutral safety switch ___ Start engine – look, listen for trouble signs, check gauges 4. With Engine Running, Check (from driver’s seat): ___ Mirrors, interior/stepwell lights, service door seal ___ Steering feel ok? Noise? ___ Steering wheel lash ___ Horn, defroster and heat blowers ___ Windshield wiper/washer operation ___ Brakes – pedal height and feel, gauge reading ok? ___ Parking brake release, reset ___ Service door control | 5. Look Inside the Bus ___ Seats, floor – housekeeping; seat belt webbing, retractor ___ Emergency exits open and close, rear door, roof, windows, warning buzzer operation ___ Emergency equipment – flares and fire axe ___ Fire extinguisher pressure ___ First aid kit – sealed ___ Driver’s area – windshield, windows – clean, cracks, bruises? ___ Wheelchair restraints, lift operation, warning lights and buzzers ___ Wheelchair door latch and retainer 6. Outside Checks Required Before You Drive Away ___ Crossing arm operation ___ Turn signal – right/left, front/rear, clean and flashing? ___ Loading lights – front/rear, clean and flashing? ___ Stop arm – clean and working? Lights flashing? ___ Daytime running lights ___ Headlights - high/low beams ___ Stoplights/taillights/marker lights/back-up lights – clean and working? ___ Hazard warning flasher working? ___ Exhaust system – leaks and security 7. Final Checks As You Move the Bus ___ Seat belt fastened? ___ Brakes. Stop and hold? ___ Clutch ok? ___ Steering feel ok? Unusual noises? ___ Bus under control/tracking straight? ___ Brake to a stop. All gauges ok? |
| --- | --- |

# Text boxes

Warning Lights

Side Windows

Windshield/

Windshield Wipers

Mirrors

Stop Arm

Engine Compartment

Tires/Wheels

Headlights

Crossing Arm

Exhaust System

Warning Lights

All Signs

Service Door

All Signals

Tires/Wheels

Emergency Rear Door

Tailpipe